## Slide 1: ENGI 301 Sound-Reactive LED Lights Proposal
October 20, 2019
Juliana Wang

## Slide 2: Background Information
Ultimate goal: LED light strip that reacts to a wav file, recorded from an AUX cord
Inspiration: DIY LED Music Visualizer | Real-Time Animations (Arduino)
Alterations to this project:
  Hardware: Staying mostly the same (PocketBeagle analogous to Arduino)
    Adding a USB audio splitter to read audio from an AUX cord and output audio to earphones or a speaker
  Software
    Recording a WAV file through an AUX cord into a USB audio splitter
    Process the WAV file into a readable array
    Use the PocketBeagle to trigger the LEDs in response to the processed array

## Slide 3: System Block Diagram
PocketBeagle
(OSD335x-SM SiP)
MicroUSB Host Connector
USB1.VIN
P1.08 GPIO 2 SPI0 CLK
Data_IN
LED Light Strip
USB Adapter
+5V
GND
P1.24 SYS VOUT
P1.22 SYS GND
P1.05 VBUS, P1.07 VIN
P1.09 DN
P1.11 DP
P1.13 ID, P1.15 GND

## Slide 4: Power Block Diagram
PocketBeagle
(OSD335x-SM SiP)
MicroUSB Host Connector
USB1.VIN
P1.08 GPIO 2 SPI0 CLK
Data_IN
LED Light Strip
5 Volts
Up to 1.3 A
5 Volts
At least 4 A
USB Adapter
+5V
GND
P1.24 SYS VOUT
P1.22 SYS GND
P1.05 VBUS, P1.07 VIN
P1.09 DN
P1.11 DP
P1.13 ID, P1.15 GND

## Slide 5: Components / Budget
Component | Need to Buy | Cost
LED Light Strips | Yes | $22.99
AUX Cord | No (OEDK) | 
USB Audio Splitter | Yes (Prof. Welsh) | 
PocketBeagle USB Adapter | No (OEDK) | 
¼” Plywood | No (scrap wood) |